## Slide 2
Sequential laboratory exercise 2 (hydraulic stand 3)
Description of function:
When operator manually operates the “dead man switch” (directional control valve no 1) the pipe valve shall close and then the brake shall be released for operation.
When the “dead man switch” (direction control valve no 1) is not operated the brake shall apply and the pipe valve open.
When operator manually operates the directional control valve no 2 in position 1 the load shall hoist.
When operator manually operates the directional control valve no 2 in position 2 the load shall lower.
When the directional control valve no 2 is no operated, the system shall stop in the current position.
The load shall be secured against pressure loss (failsafe system)
Max. system pressure: 85 bar.
Pipe valve pressure: min. 60 bar max. 80 bar
Brake pressure: min 60 bar max. 80 bar
Draw the hydraulic circuit.
Connect the hydraulic system using the necessary components.
Set the system so the functionality is as described.