## Slide 1: SIMAC Hydraulic 2
Basic Hydraulic – Check Valves

## Slide 2: Basic Hydraulic Check Valves
Notes: Check valve are used in hydraulic systems to mainly stop flow in one direction and to allow free flow in the opposite direction.
They are also known as non-return valves.
Check valves are designed with seats and hence are able to isolate circuits with no leakage

## Slide 3: Basic Hydraulic Check Valves
Valve design
  Ball
  Poppets
Simple Check Valve
  Rectifier circuit
Pilot operated check valve
  Without drain port
  With drain port
Double pilot operated check valve (Load holding valve)

## Slide 4: Basic Hydraulic Check Valves – Valve design
Advantage: Produced economically
Disadvantage: Ball is deformed during operation causing internal leaked due to the seat is not pressed onto the same point
Notes: Check valve Ball type

## Slide 5: Basic Hydraulic Check Valves – Valve design
Advantage: Poppets always resume the same position due to their control, the seat and the valve is completely sealed.
Disadvantage: Production is more technically advanced
Notes: Check valve Poppet type

## Slide 6: Basic Hydraulic Check Valves – Simple Check Valve
Check valves are used
  For bypassing throttling points
  For closing one direction flow
  As bypass valves, e.g. for bypassing a return line filter when a particular back pressure has been reached
  As pretension valves (holding valves) to create a certain backpressure in an operating cycle
Notes: The opening pressure of an check valve depends of the spring load and the pressurized poppet surface area. It is generally between 0.5 to 10 bar depending on the application
Check valves without spring must always be installed vertically

## Slide 7: Basic Hydraulic Simple Check Valve – Rectifier circuit
Notes: The rectifier circuit is a special design that is mainly used together with flow control valves or pressure control valves
Can be used together with i.e. a single acting cylinder

## Slide 8: Basic Hydraulic Pilot operated check valve – Without drain port
Notes: Pilot operated check valve
Free flow from A to B
Pilot pressure must over win the pressure acting on annulus side of the pilot piston from port A to make the valve open. In practice this means that there must not be pressure on port A.
It make sense to use these valves if port A is at zero pressure when the control valve is open

## Slide 9: Basic Hydraulic Pilot operated check valve – Without drain port
Notes: Pressure on port A is equal to tank pressure when control valve is to the left, meaning pilot port pressure is highest
It make sense to use these valves if port A is at zero pressure when the control valve is open

## Slide 10: Basic Hydraulic Pilot operated check valve – With drain port
Notes: Pilot operated check valve – With drain port
In contrast to a pilot operated check valve without case drain port, the annular area of the control piston is separated from port A. Pressure at port A affects only surface A4 of the control piston
Pilot pressure can be less than for at check valve without case drain port.
These valves must be used if port A is under pressure when the control valve is opened
The check valve is used to avoid compression shocks. When port X is pressurized the pilot piston will first open the check valve, and then the main poppet.

## Slide 11: Basic Hydraulic Pilot operated check valve – With drain port
Notes: In contrast to a pilot operated check valve without case drain port, the annular area of the control piston is separated from port A. Pressure at port A affects only surface A4 of the control piston
Pilot pressure can be less than for at check valve without case drain port.
These valves must be used if port A is under pressure when the control valve is opened

## Slide 12: Basic Hydraulic Double pilot operated check valve
Notes: This can be used to hold the load of a cylinder.

## Slide 13: Basic Hydraulic Double pilot operated check valve

## Slide 14: Basic Hydraulic Check Valves - More information
Video
  Check valves 02:04 AVSEQ12
Notes: 12 02:04 Kontraventiler, holde last, leaks in slide valves
pilotstyret, animationer

## Slide 15: Basic Hydraulic Exercise - Automation Studio
  Exercises
    Exercise 4.1 - Check valve without case drain port
    Exercise 4.2 - Double pilot operated check valve
Notes: Fig 7.5 – Double rod cylinder
Fig 7.6 – Differential double rod cylinder
F=p•A F=m•g