## Slide 1: SIMAC Hydraulic 2
Basic Hydraulic - Cylinders

## Slide 2: Basic Hydraulic Cylinders

## Slide 3: Basic Hydraulic Cylinders
Cylinder types
  Single-acting cylinder
  Double-acting cylinder
  Exercise Automation Studio
Special types of single- and double-acting cylinders
  Tandem
  Traverse
  Telescopic
Basic principles of cylinder design
  Tie rod cylinders
  Mill type cylinders
Notes: Due to their function, it is possible to categories cylinders into two groups
- Single acting Cylinders
- Double acting cylinders

## Slide 4: Basic Hydraulic Single acting cylinders
Single acting cylinders can only exert force in one direction. The piston can only be returned by a spring, through the weight of the piston itself or by the action of an external force. Single acting cylinders basically have only one effective area.
Two type of single acting cylinders
  Plunger cylinder
  Spring return cylinders
Notes: F=p•A F=m•g

## Slide 5: Basic Hydraulic Single acting cylinders – Plunger type
  Plunger cylinders are used wherever a definite direction of external force will definitely return the piston to its starting position
    Upstroke presses
    Cutter stroke tables
    Lifting devices
Notes: F=p•A F=m•g
Plunger cylinders can be constructed with or without internal stroke limiter…

## Slide 6: Basic Hydraulic Single acting cylinders – Spring return type
  Cylinders with spring return is used where an external restoring force does not exist. Springs are mainly found in small cylinders used in installation work or tools
Notes: Fig 7.2 – Single-acting push action cylinders Left: with internal spring . Right: With external spring
Fig 7.3 - Single-acting pull action cylinders Left: with internal spring . Right: With external spring
F=p•A F=m•g

## Slide 7: Basic Hydraulic Double acting cylinders
Double acting cylinders have two opposing effective areas which are of the same or different size. This type of cylinder is found in nearly all type of application.
Two type of double acting cylinders
  Single rod cylinder
  Double rod cylinders
Notes: F=p•A F=m•g

## Slide 8: Basic Hydraulic Double acting cylinders – Differential cylinders (Single rod)
  The area ration of piston area to annulus area is indicated by the factor φ.
Notes: Differential cylinders is also called single rod cylinders
The name comes from the fact that they have different sizes of the effective area.
The extend and retraction velocity is different due to the fact of difference volumes.
The retraction force is smaller than extended force due to at smaller area in annulus
F=p•A F=m•g

## Slide 9: Basic Hydraulic Double acting cylinders – Double rod
Notes: Fig 7.5 – Double rod cylinder
Fig 7.6 – Differential double rod cylinder
F=p•A F=m•g

## Slide 10: Basic Hydraulic Exercise - Automation Studio
  Exercises
    Exercise 3.1 – Single rod cylinder
    Exercise 3.2 – Double rod cylinder
Notes: Fig 7.5 – Double rod cylinder
Fig 7.6 – Differential double rod cylinder
F=p•A F=m•g

## Slide 11: Basic Hydraulic Special types of cylinders – Tandem cylinder
Notes: Certain applications exist where standard single or double acting cylinders may only be used by taking special additional measures involving a lot of effort. The most common of these cases is where long strokes are needed with extremely little installation room or where large forces is required for the smallest piston diameter.
This and other requirements has led to the design of a series of special models which are partly more difficult and take more effort to produce.
Tandem cylinders are used where a large force are needed in a small installation area
The two area are added together and thereby larger forces may be transferred for relative small external diameters without increasing the diameter.
F=p•A F=m•g

## Slide 12: Basic Hydraulic Special types of cylinders – Rapid traverse cylinder
  Rapid traverse cylinders are primarily used in presses.
  Advantages:
    High rapid traverse velocity due to small volume
    High pressing force due to large effective piston area
Notes: Single acting Rapid traverse cylinder
As long a the complete work force is not required only part of the effective area is pressurized.
Fig. 7.8 - (<=) Rapid traverse via port A1 (Suction via connection port S)
- (<=) Pressing force via port A2
- (=>) Retracting movement via weight of piston itself or though external force being applied, return from A1 and A2
F=p•A F=m•g

## Slide 13: Basic Hydraulic Special types of cylinders – Rapid traverse cylinder
  Rapid traverse cylinders are primarily used in presses.
  Advantages:
    High rapid traverse velocity due to small volume
    High pressing force due to large effective piston area
Notes: Double acting rapid traverse
As long a the complete work force is not required only part of the effective area is pressurized.
Fig. 7.9 - (<=) Rapid traverse via port A1 (Suction via connection port S)
- (<=) Pressing force via port A2
- (=>) Retracting movement via port B, return from A1 and A2
F=p•A F=m•g

## Slide 14: Basic Hydraulic Special types of cylinders – Telescopic cylinders
  The piston with the largest effective area extents first.
  At constant pressure and flow, the extension begins with the largest force and smallest velocity and finishes with the smallest force and highest velocity.
Notes: Single acting Telescopic cylinder
Telescopic cylinders vary from normal cylinders in that they only need a very small amount of space to be installed on, when the are retracted compared with normal cylinders with the same stroke.
Fig. 7.10 - Stroke force must be designed in accordance with the smallest effective piston area
F=p•A F=m•g

## Slide 15: Basic Hydraulic Special types of cylinders – Telescopic cylinders
  The order in witch the individual stages are retracted depend on the size of the annulus area and on the external load.
Notes: Double acting telescopic cylinder
F=p•A F=m•g

## Slide 16: Basic Hydraulic Basic principles of cylinder design – Tie rod cylinders
  As these cylinders are compact and space saving, they are primarily used in machine tool industry and in manufacturing devices.
Notes: The physical design of all the above mentions cylinder variants depending of the design type.
The top of the cylinder, the cylinder barrel and the bottom of the cylinder are all connected together via a tie rod
F=p•A F=m•g

## Slide 17: Basic Hydraulic Basic principles of cylinder design – Tie rod cylinders
Notes: 20) Check valve – Help cylinder when retracted, feeding oil into the large champer
21) Throttle valve – The cushioning effect is set at the throttle valve, the smaller the flow area is the larger is the effect of cushioning at the end position
F=p•A F=m•g

## Slide 18: Basic Hydraulic Basic principles of cylinder design – Tie rod cylinders
Notes: 20) Check valve – Help cylinder when retracted, feeding oil into the large camper
21) Throttle valve – The cushioning effect is set at the throttle valve, the smaller the flow area is the larger is the effect of cushioning at the end position
F=p•A F=m•g

## Slide 19: Basic Hydraulic Basic principles of cylinder design – Mill type cylinders
  Due to its robust design, hydraulic mill type cylinders are suitable for use in application with extreme operating conditions.
Notes: Mill type cylinders
The head an base of the cylinder and cylinder barrel are screwed, welded or connected tightly via bolds or retaining rings.
F=p•A F=m•g

## Slide 20: Basic Hydraulic Basic principles of cylinder design – Mill type cylinders
Notes: 19) Check valve – Help cylinder when retracted, feeding oil into the large camper
20) Throttle valve – The cushioning effect is set at the throttle valve, the smaller the flow area is the larger is the effect of cushioning at the end position
F=p•A F=m•g

## Slide 21: Basic Hydraulic Basic principles of cylinder design – Mill type cylinders
Notes: 19) Check valve – Help cylinder when retracted, feeding oil into the large camper
20) Throttle valve – The cushioning effect is set at the throttle valve, the smaller the flow area is the larger is the effect of cushioning at the end position
F=p•A F=m•g

## Slide 22: Basic Hydraulic Cylinders - More information
Video
  Hydraulic cylinders 07:03 AVSEQ09
Notes: 09 07:03 Actuatorer, cylindre, motorer, animationer af single
acting, double acting, eksempler på anvendelse
(autolift, værktøjsmaskine) double rod, servostyring
teleskop cylinder, tandhjulsmotor animation