## Slide 1: SIMAC Hydraulic 2
Basic Hydraulic – Pressure Control Valves

## Slide 2: Basic Hydraulic Pressure Control Valves
Notes: Pressure control valves are valves which influence the system pressure in a system or part of a system in a predetermined manner. This is achieved by changing the size of throttle opening at metering notches.
Pressure control valves has two positions. A changes of position occurs abruptly (by switching) or gradually (by control) though the effect of one or several pressures on one or more surfaces of the spool and against the springs.

## Slide 3: Basic Hydraulic Pressure Control Valves
Subdivision of Pressure control valves
  Pressure relief valves
    Direct and pilot operated
  Pressure sequence valves
    Direct and pilot operated
  Pressure shut-off valves
    Pilot operated
  Pressure reducing valves
    Direct operated

## Slide 4: Basic Hydraulic Pressure Control Valves
Notes: The Pressure control valves are divided into groups according to their function
Pressure control valves are available in following designs
- Depending on the sealing of the throttle opening as a spool valve or at poppet valve
- Depending on the control as a directly or pilot operated valve
- Depending on the mounting

## Slide 5: Basic Hydraulic Pressure Control Valves – Pressure relief valves – Directly operated
Poppet valve type
Notes: Poppet valve type
When the pressure relief valve opens, hydraulic energy is converted to heat:
W = Δp•Q•t
The poppet valve type provides hermetic, leak-free sealing and quick response time, because of large flows may be removed with small stroke movements

## Slide 6: Basic Hydraulic Pressure Control Valves – Pressure relief valves – Directly operated
Spool valve type
Notes: Spole valve type
When the pressure relief valve opens, hydraulic energy is converted to heat:
W = Δp•Q•t
The spool valve type offers fine control of small flows by means of the grooves in the spool.
A small leak flow will always flow trough the gap and the response time is higher than for at poppet valve type due to that the spool must travel the distance s before it opens.

## Slide 7: Basic Hydraulic Pressure Control Valves – Pressure relief valves - Directly operated
Cushioning possibilities for directly operated pressure relief valves to prevent oscillations in the system.
Damping spool and orifice to spool chamber
Damping spool with one surface
Damping spool with correspondingly large tolerance play

## Slide 8: Basic Hydraulic Pressure Control Valves – Pressure relief valves - Directly operated
Notes: Directly operated refers to that the opening pressure is adjusted via the spring acting against the main pressure.
Control block
Comprises sleeve
Spring
Adjustment mechanism
Poppet with damping spool
Hardened seat
Damping bore
Spring retainer

## Slide 9: Basic Hydraulic Pressure Control Valves – Pressure relief valves – Pilot operated
Notes: Pilot operated refers to that the opening pressure is adjusted via the spring acting against the pilot pressure.
The advantage of the pilot operated pressure relief valve is that for the same operating pressure the physical size of the valve is smaller due to that the spring load (pilot) is smaller for the same flow.

## Slide 10: Basic Hydraulic Pressure Control Valves – Pressure relief valves – Pilot operated
Notes: Pilot operated pressure relief valve for sub-plate mounting
Pilot operated refers to that the opening pressure is adjusted via the spring acting against the pilot pressure.
The advantage of the pilot operated pressure relief valve is that for the same operating pressure the physical size of the valve is smaller due to that the spring load (pilot) is smaller for the same flow.
The valve on the picture can ether be operated with external pilot pressure or by closing port x and insert an orifice position 4.

## Slide 11: Basic Hydraulic Pressure Control Valves – Pressure relief valves – Pilot operated
Notes: Pilot operated pressure relief valve with discharge
One typical example of application is the pressure-free start of a pump
Free circulation is achieved when the directional control valve is energised.
- main spool chamber (1) on the spring side is connected to channel T (2) of the directional control valve
Operates as a pressure relief valve when the directional control valve is deenergised.
- The is no connection from the spring side to port B

## Slide 12: Basic Hydraulic Pressure Control Valves – Sequence valves – Directly operated
Notes: Directly operated pressure sequence valve
Pressure sequence valves is also known as Bypass valves Pre-load or deceleration valves are similar in design as pressure relief valves.
Pressure sequence valves are situated in the main flow of the hydraulic system and switch on and off further hydraulic systems when a set pressure is reached.
Basically pressure relief valves may also be used as pressure sequence valves. The pre-requisite for this is that the pressure in channel T (directly operated pressure relief valve) or in channel B (Pilot operated pressure relief valve) cannot change the preset value. This is achieved by feeding the leaked oil externally and pressure free to tank.
A check valve may be optionally build in to the system to allow free return flow from channel A to channel P.

## Slide 13: Basic Hydraulic Pressure Control Valves – Sequence valves – Directly operated
Notes: Directly operated pressure sequence valve
Pressure sequence valves is also known as Bypass valves Pre-load or deceleration valves are similar in design as pressure relief valves.
Pressure sequence valves are situated in the main flow of the hydraulic system and switch on and off further hydraulic systems when a set pressure is reached.
Basically pressure relief valves may also be used as pressure sequence valves. The pre-requisite for this is that the pressure in channel T (directly operated pressure relief valve) or in channel B (Pilot operated pressure relief valve) cannot change the preset value. This is achieved by feeding the leaked oil externally and pressure free to tank.
A check valve may be optionally build in to the system to allow free return flow from channel A to channel P.

## Slide 14: Basic Hydraulic Pressure Control Valves – Sequence valves – Pilot operated
Notes: Pilot operated pressure sequence valve – internal pilot oil feed, internal pilot oil drain
A check valve may be optionally build in to the system to allow free return flow from channel A to channel P.

## Slide 15: Basic Hydraulic Pressure Control Valves – Shut-off valves – Pilot operated
Notes: Pressure shut-off valves
Pressure shut-off valves also known as accumulator charging valves, are mainly used in hydraulic systems with accumulators. Main task is to switch pump flow to pressure-free flow once the accumulator has reached its charging pressure.
Change of pump flow from P -> A to P -> T
The hydraulic pump delivers fluid to the system via check valve (4). Pressure present in channel A acts on pilot spool (6). Pressure in channel P acts on the spring load side of main spool (3) and ball (9) in pilot valve (2) via orifices (7) and (8).
When shut-off pressure is reached ball (9) open against the spring (10), fluid flows via orifices (7) and (8) into spring camper (11). From here, fluid is fed to tank an port P is then connected to port T
Change of pump flow from P -> T into P -> A
The surface of the pilot spool (6) is approx. 10% larger than the effective surface of the ball.

## Slide 16: Basic Hydraulic Pressure Control Valves – Reducing valves – Directly operated
Notes: Pressure Reducing valves
In contrast to pressure relief valves pressure which affects the level of input pressure (pump pressure), pressure reducing valves are used to influence the output pressure (actuator pressure)

## Slide 17: Basic Hydraulic Pressure Control Valves – Reducing valves – Pilot operated
Notes: Pressure Reducing valves
In contrast to pressure relief valves pressure which affects the level of input pressure (pump pressure), pressure reducing valves are used to influence the output pressure (actuator pressure)

## Slide 18: Basic Hydraulic Cylinders Pressure Control Valves - More information
Video
  Pressure valves 04:29 AVSEQ13
Notes: 13 04:29 Trykventiler, relief: animation, regulator: animation
3 vejs regulator

## Slide 19: Basic Hydraulic Exercise - Automation Studio
  Exercises
    Exercise 5.1 – Pressure relief valve
    Exercise 5.2 – Pressure sequence and pressure reducing valve
Notes: F=p•A F=m•g