## Slide 1: SIMAC Hydraulic 2
Basic Hydraulic – Flow Control Valves

## Slide 2: Basic Hydraulic Flow Control Valves
Notes: Flow control valves are used to influence the speed of movements of actuators by changing the opening to flow at the throttling point.

## Slide 3: Basic Hydraulic Flow Control Valves
Flow control valves
  Overview of types
  Throttle valves
    Dependent on viscosity
      Deceleration valve
    Independent of viscosity
  Flow control valves
    2 – Way (Dependent on viscosity)
      Meter- in / Meter-out / bypass flow control
    3 – Way (Independent of viscosity)

## Slide 4: Basic Hydraulic Flow Control Valves – Overview of types
Notes: As we have see previously with directional control valves the Flow control valves can also be divided into types depending on the design.
Flow control valves are used to influence the speed of movements of actuators by changing the opening to flow at the throttling point.
Flow dividers has a certain special standing. They divide an oncoming flow into two or more flows.
Throttle valves
- dependent of viscosity
- independent of viscosity
Flow control valves
- dependent of viscosity
- independent of viscosity
Depending on their behavior, flow control valves may be divided into 4 groups.

## Slide 5: Basic Hydraulic Flow Control Valves – Throttle Valves – Dependent on viscosity
Notes: Throttle point is formed between the housing and adjusted sleeve (4)
This type is throttling in both directions
The flow can be adjusted by turning the house
When the fluid is heated due to operation of the hydraulic system the viscosity of the fluid is decreased. When the viscosity is decreased the flow will increase due to the formulas at page 230

## Slide 6: Basic Hydraulic Flow Control Valves – Throttle Valves – Dependent on viscosity
Notes: Throttling in one directions
Check valve in the other direction

## Slide 7: Basic Hydraulic Flow Control Valves – Throttle Valves – Dependent on viscosity
Notes: Throttle valves with mechanical operation are used for path-dependent smooth deceleration or acceleration of hydraulically.
In order to allow the cylinder to travel out of the closed position, a check valve (6) can be arranged parallel to the throttle spool. It ensures free flow from B to A.
The cylinder then extends from its position without restriction. If a check valve is not present, acceleration occurs when travelling out of the end position. Se page 236

## Slide 8: Basic Hydraulic Flow Control Valves – Throttle Valves – Independent of viscosity
Notes: Independent of viscosity
The low dependence on temperature is due to throttling position being an orifice (the throttling path is almost zero) (see formulas at page 230 equation 3 ) . The preferred direction of flow is from A to B.
Flow can be adjusted by turning bolt cam (5)

## Slide 9: Basic Hydraulic Flow Control Valves – 2-Way Flow control valve
Notes: Flow control valves (constant pressure drop => constant flow [Bernoulli’s equation])
Flow control valves are used to keep a set constant flow regardless of pressure variations. In addition to the adjustable throttle (A2) (measuring throttle) an additional moving throttle (Ak) is build into the system, which operates as a control throttle (pressure compensator)
As the path of the control spool is approx < 1mm and the spring is soft, the change in spring force with respect with respect to spool path may be neglected and hence dp or Q is constant.
The valve can not start working until the external pressure difference P1 – P3 is greater than FK/AK

## Slide 10: Basic Hydraulic Flow Control Valves – 2-Way Flow control valve
Meter-in flow control
Notes: This type of control is recommended for hydraulic systems in which the actuator counters the controlled flow with a positive resistance
Advantage
Pressure present between flow control valve and cylinder depends on the working load, therefore less pressure on cylinder seal meaning lower friction from the sealing rings.
Disadvantage
Because the pressure relief valve is upstream of the flow control valve, it must be set to the highest actuator pressure. Due to this the pump always delivers against the maximum set pressure.
Heat from flow control valve is lead to actuator.

## Slide 11: Basic Hydraulic Flow Control Valves – 2-Way Flow control valve
Meter-out flow control
Notes: This type of control is recommended for hydraulic systems with negative or pulling working loads.
Advantage
No counterbalance valve is required, the heat from the throttle is led to the tank
Disadvantage
Pressure relief valve must be set to the highest actuator pressure. Due to this the pump always delivers against the maximum set pressure.
All elements in the cylinder is under maximum pressure (higher friction)

## Slide 12: Basic Hydraulic Flow Control Valves – 2-Way Flow control valve
Bypass flow control
Notes: The flow control valve only controls the flow being fed to the cylinder to a limited extent, as a set portion of the pump delivery flow is returned to the tank.
Advantage
Only the pressure required for the load is build up during the stroke, meaning less power is converted to heat.
It’s not until the cylinder runs against the stop that the pressure set on the pressure relief valve is reached

## Slide 13: Basic Hydraulic Flow Control Valves – 3-Way Flow control valve
Notes: In contrast to a 2-way flow control valves, the measuring orifice A2 and the control orifice A1 are connected in parallel.
The pressure compensator controls the excess flow via an additional line to tank. A pressure relief valve must be included in the hydraulic circuit to protect the maximum pressure, this is normally already integrated into the 3-way flow control valve.
A 3-way flow control valve has smaller power losses, a better degree of efficiency in the system and less heat is created that a 2-way flow control valve

## Slide 14: Basic Hydraulic Flow control valves - More information
Video
  Flow control valves 04:28 AVSEQ14
Notes: 14 04:28 Flow control valves sammen med relief, animation, last
afhængighed, trykkompenseret (vises modsat Bosch-bogen
med kompensatoren EFTER drøvlingen) drøvling på + eller
- ledning

## Slide 15: Basic Hydraulic Exercise - Automation Studio
  Exercises
    Exercise 7.1 – Flow control valve
Notes: F=p•A F=m•g