## Slide 1: SIMAC Hydraulic 2
Basic Hydraulic – Hydraulic Principles

## Slide 2: Basic Hydraulic Hydraulic Principles
Physics terms
  Force
  Pressure
Hydrostatic
  Pressure –The Hydrostatic paradox
  Pressure –Pascal’s Law
  Force transmission
  Pressure transmission
  Flow law
Friction and Pressure losses
  Pressure Losses
  Types of flow

## Slide 3: Basic Hydraulic Physic terms - Force
Newton’s 2. Law of motion
  If general acceleration a is replaced by acceleration of gravity g the following is obtained
Notes: All the following examples is loss free, meaning that all the energy is convertet from one stages to another without losses to the surroundings !!!
Explain the equation using SI units
- m [kg]
- a [m/s2]
- F [kg*m/s2=N]
- FG = Weight forse
and give an example on the whiteboard
- Man with a weight of 100 kg will resulte in a Force of 9.81x100=981 N
In practice it is general adequate to use g=10N = 1dN

## Slide 4: Basic Hydraulic Physic terms - Pressure
If a force acts perpendicularly to a surface, then the force F divided by the area of the surface A is the pressure p.
Notes: Explain the equation and give an example on the whiteboard
- Man with a weight of 100 kg will resulte in a Force of 9.81x100=981 N (1000 N)
- If we place the man on top of a cylinder with a diameter of 20 mm (0,02 m2) the pressure would be
A= (pi/4)*d2 = (3.14/4)*0.0202 = 0.000314 m2
p=1000/0.000314 = 3124203 PA = 31.24 bar
1 bar = 14.50 PSI (pounds per square inch)
pPSI = 3.97*14.50= 58 PSI
In practice it is general adequate to use g=10N = 1dN

## Slide 5: Basic Hydraulic Hydrostatics- Pressure – The Hydrostatic paradox
Notes: Witch force is the greatest due to the amout of oil?
They are equal due to the same pressure hight of the fluid, even though the amount of fulied is not the same (volume = mass)
The pressure is the same due to p=rho*g*h
rho= density
that means that p*A1 is equal to p*A2 and to p*A3 so F1=F2=F2
even though the amount of fluid isn’t the same in the containers

## Slide 6: Basic Hydraulic Hydrostatics- Pressure – Pascal’s Law
“The effect of a force acting on a stationary fluid spreads in all directions within the fluid. The amount of pressure in the fluid is equal to the weight force, with respect to the area being acted upon. The pressure always act at right angles to the limiting surface of the container”
Notes: Pascal found that…Pressure due to external forces…
Weight force = m*g

## Slide 7: Basic Hydraulic Hydrostatics- Pressure – Pascal’s Law
Notes: Pressure act equally on all sides.
Neglecting pressure due to gravity, pressure is equal at all points. (This can be done in modern hydraulic due to the high operational pressures)
p=F/A

## Slide 8: Basic Hydraulic Hydrostatics- Force transmission
Notes: Force Transmission (constant pressure)
Calculate on the witeboard the relationship between F1,A1 and F2, A2
P= F1 /A1 Pressure act at every point of the system meaning F2 = p • A2
F1 /A1 = F2 /A2  F1 /F2 = A1/A2 The forces are in the same ration as the areas
s1 /s2 = A2 /A1 distance the pistons will travel behave in inverse proportional to the areas
Area of Circle A=(pi/4)*d2
Give an excample
m1 =100 kg 100 kg
d1 = 20 mm 50 mm
d2 = 1000 mm 1000 mm
F1 = 981 N 981 N
F2 = 2452500 N 392400 N
m2 =245250 kg 3924 kg

## Slide 9: Basic Hydraulic Hydrostatics- Pressure transmission
Notes: Pressure Transmission (constant Force)
Can be used to step up pressures in hydraulic systems
Instead of transmitting different forces we can transmit different pressures
Two pistons of different sizes are connected by means of a rod.
If area A1 is pressurised with pressure p1 a force F1 is transfered via the rod to area A2 and course pressure p2
F1 = F2
F1 = p1 • A1 ; F2 = p2 • A2
Give excample
d1 = 1000 mm 1000 mm
d2 = 20 mm 50 mm
P1 = 10 bar 10 bar
p2 = 25000 bar 397 bar
p1 /p2 = A2 /A1
In pressure transmission units the pressure behave in inverse proportion to the areas.

## Slide 10: Basic Hydraulic Hydrostatics – Flow Law
Notes: Flow law
Equal volumens flow through a pipe of varying diameters over the same period of time. This means that the flow velocity of the fluid must increase at a narrow point.
Q1=Q2
Q1= A1•v1
A1•v1 = A2•v2
It can also be shown that the pressure drops when the velocity increase, due to
Bernoulli’s equation, with respect to pressure energy. (the law of conservation of energy)

## Slide 11: Basic Hydraulic Friction and Pressure losses
So far we have assumed that there is no friction between fluid layers as they move against each other and also that there is no friction as fluids move against a body.
Notes: Hydraulic Losses
However, hydraulic energy cannot be transfered througt pips without losses. Friction occure at the pipe walls and within the fuilds, generating heat. The loss created in this way in hydraulic energy actualy means that a pressure loss occurs within the hydraulic system.

## Slide 12: Basic Hydraulic Friction and Pressure losses – Pressure Losses
The size of the pressure loss (frictional loss) is mainly dependent on:
  Length of pipe
  Cross- section area of pipe
  Roughness of pipe walls
  Number of pipe bends
  Velocity of flow
  Viscosity of the fluid
Notes: We can take a closer look at pressure loss

## Slide 13: Basic Hydraulic Friction and Pressure losses – Pressure Losses
Notes: When the velocity is to high the flow will no longer be laminar, it will become turbulent. This result in increased flow resistent and thus the hydraulic losses increase.
Therefor turbulent flow is usually not disirable.

## Slide 14: Basic Hydraulic Hydraulic Principles - Summary
Physics Terms
  Force
  Pressure
Hydrostatics
  Pressure – The Hydrostatic paradox
  Pressure – Pascal’s Law
  Force transmission
  Pressure transmission
  Flow law
Friction and Pressure losses
  Pressure Losses
  Types of flow
Notes: Force: F=m•g
Pressure: P=F/A
Pascal’s law: “The effect of a force acting on a stationary fluid spreads in all directions within the fluid. The amount of pressure in the fluid is equal to the weight force, with respect to the area being acted upon. The pressure always act at right angles to the limiting surface of the container”
  Force transmission (constant pressure): F2/F1=A2/A1 s1/s2=A2/A1
  Pressure transmission (constant force): p1/p2=A2/A1
  Flow law: A1•v1=A2•v2

## Slide 15: Basic Hydraulic Hydraulic Principles - UNITS
Pressure
1 Bar = 14.5038 PSI
Force
1 Nm = 0.2248 pounds-force
http://en.wikipedia.org/wiki/Pound-force

## Slide 16: Basic Hydraulic Hydraulic Principles - More information
Video
  Pascal’s Law 02:45 AVSEQ03
  Force balance 01:40 AVSEQ04
  Flow velocity 02:15 AVSEQ06
Notes: 03 02:45 p=F/A, Pascals lov, cylinderhastighed vs. flow, Q=V/t
eksempel med cyl. hast. ved forskellige flow
04 01:40 To stempler med lodder på, kraftbalance, arealforhold,
donkraft
06 02:15 Forskellige rørtværsnit => forskellige hastigheder,
laminært flow, trykfald i indsvævringer, kavitation,
billede af kaviteret komponent, gennemsigtige
komponenter, dieseleffekt